GPS

# Declaration

# Welcome to use the GPS navigator!

# The product is subject to change without prior notice. We apologize for any inconvenience caused.

# Our company assumes no liability for data missing caused by users who did not backup the important information.

# This manual has been checked with thorough care, but we do not exclude the possibility of a few unintended errors. If you spot an error, please contact our customer service center.

# Please read the operations and instructions in this User Manual carefully and use accessories provided by the original manufacturer only, avoiding unexpected damages. Implementing the system without conforming to proper programs or connecting incompatible accessories may result in the invalidity of a warranty and even endanger the safety of you and others. The company assumes no liability for the result.

# The development of the traffic construction may lead to the in conformity of the data of the navigable electronic map with actual traffic instructions. Please drive according to current traffic regulations, including current road conditions and current marks. Viewing or operating a navigator while driving may cause serious traffic accidents. The company assumes no liability for the accidents or any corresponding losses.

In case there is any divergence between the pictures in this manual and the real products, the real products will prevail.

# Precautions

01. Do not shake or knock the device. Rough handling may lead to damage or missing of the data and failures to play files.

02. Keep the device away from direct sunlight or high temperature, to prevent overheating of the batteries and device body which may cause failures or dangers.

03. Keep the device away from moisture and raindrops. If water gets inside, the wet condition may cause the device to break down or even render it beyond repair.

04. Do not disconnect the device by self.

05. Keep the device away from sand dusts or environment of dusts.

06. Operating the device near strong radio wave or radioactive rays may affect the performance of the device.

07. Insert the plug fully into the electrical outlet to prevent static electricity.

08. Ensure that all cables are connected to the device safely and orderly, to prevent falling and damages of the device caused by the messy arrangement.

09. Do not press the LCD screen hard; keep the LCD screen away from sunlight, or failures to the device may occur. Clean up dusts on the screen surface with soft cloth.

10. If the device fails, please send it to an authorized mountaineer for repair.

11. Backup the data on the SD/MMC card to a computer regularly, to prevent the risk of data missing.

12. Pay attention to the compatibility of media files. Only files conforming to the design rules of the device can be played.

13. Films, music, and images may be copyrighted. Playing those files without permission would violate the copyright law

14. Do not use metal objects to short-circuit a charger or device input. This may result in device failures.

15. Keep the device away from heat source.

16. Operate the device by placing it on a level desk. Operating by placing it on a blanket, pillow, or carpet will render working temperature too high for the device, and may damage it.

17. When the system executes the read-write operation for the memory card, do not take it out, or data in the card may be destroyed or missing. This may even cause the system to break down.

18. Do not power off when you are navigating, playing films and music, and viewing pictures.

19. Do not store the batteries or charge the batteries in cold or hot areas, or the performance of the batteries may be damaged.

20. Keep the battery or charger out of the reach of children.

21. Mistakes in changing batteries may cause an explosion. Dispose the old batteries according to instructions.

22. Use the battery specified by the original manufacturer on changing batteries.

23. Keep the device out of reach of children when it is being charged.

24. Violent collision or drop may damage the device or spoil its appearance. Please take care.

25. Do not use an earplug with over high volume, or it will hurt your hearing and even cause permanent hearing impairment.

26. Please do not set the volume of an external loudspeaker too high for a long time. Longstanding use may cause an output distortion of the loudspeaker.

27. While watching videos, repetitive actions may result in discomfort in hands, arms, shoulders or other parts of your body.

28. Decrease the brightness and volume to make the battery work longer.

Welcome to use the navigator. Centered on GPS navigation function, the navigator supports such optional functions as video playing, audio playing, image viewing, Ebook reading, and Bluetooth (optional) etc.

The application of processor features high performance.

The user-friendly interface features simple and easy operation.

Power management guarantees reliable and durable service of the product.

Data transmission: Communicate with a computer via USB interface.

Excellent reception: Accurate positioning provides satisfied navigation service.

Entertainment provider: digital TV/MP3/MP4 entertainment functions can relieve your tiredness.

You can use it almost anywhere and anytime, like when driving, walking, bicycling or waiting for a meeting. The perfect “GPS + entertainment” functions provide you with a colorful work and life.

## 1.1 Packing List

Make sure all the items are included in the package of the navigator:

Main equipment    User manual & Guarantee card     Vehicle power adaptor

USB cable      		       Touch Pen		   	     Bracket

In case there is any divergence between the above and the real products, the real products will prevail.

For any defective items, please contact your dealer or agent who sold you the product as soon as possible.

1.2 How to Use This Manual

To make best use of the navigator, read the Product Manual thoroughly to know the operation details.

While reading, you may see some supplement as following:

[Note]: This indicates corresponding interpretation or explanations.

[Reference]: This indicates corresponding extended information.

[Caution]: This indicates corresponding notices and warnings. Please place importance on the information and follow the corresponding instructions, or it may cause destructive impact against you and other people.

The Product Manual applies to the navigator only.

2 Introduction

This chapter provides information on the external elements and basic instructions, allowing you to get familiar with the basic operations.

2.1 Product Appearance

| 1 | Power Key | This is used to power on/off the system. |
| --- | --- | --- |
| 2 | Touch Pen | This is used to click and write on the screen; take it out for using and put it backafterward. |
| 3 | Loudspeaker | This is used to play audio, like navigation prompt voice and music. |
| 4 | Bracket | This is used to brase the unit on the table-board. |
| 5 | Reset | This is used to restart the system. |
| 6 | Indicator Light | Bluelight indicates Bluetooth function (Keep light indicates connecting with the unit, flicker indicates disconnecting with the unit); Red light indicates charging; Green light indicates the charging is complete. |
| 7 | Earphone slot | This is used to connect a stereo earphone. |
| 8 | TF/MMC Card Slot | Inside holds a TF/MMC memory card that stores the map software, map data, and user files. Do not take if out during operation. [Caution] If you pull out the card accidentally, press the reset key to activate the system again. |
| 9 | USB Interface | This is used to communicate with a computer via the USB cable. |
| 10 | AV-IN | This is used to connect with the car rearview system. |

2.2 Power Supply and Charging of a Navigator

When the GPS navigator is used for the first time or no used for a long time, the butteries must be completely charged with a USB cable.

2.2.1 Power supply

The navigator can be powered in two ways, i.e. batteries and the chagrer adaptror.

When not connected to the charger adapter, the GPS navigator is powered by the lithium batteries. The power icon [  ] on the top right corner of the system interface indicates the remaining battery power.

When connected to the charger adapter, the GPS navigator is powered by the external power.

[Note] This navigator uses built-in, not the removable lithium polymer battery power supply. Generally (for example, backlight brightness setting is low), completely fills the electricity, the battery can supply power continually about for 3 hours. It regards you to use the GPS to decide, battery's actual supply time will be different. Some functions (audio, video, high luminance back light) must consume the massive electrical energies, will obviously reduce power supply time.

[Caution]Do not disassemble, pierce, collide or discard the battery in the fire or water. The battery can burst, blast, or release danger chemical substance.

2.2.2 Charging with a power adapter

Used for the first time or no used for a long time, the GPS navigator must be completely charged by a USB charger adaptor.

1. Connect the DC terminal of the adapter to the power terminal on the bottom side of a GPS navigator.

2. Connect the other terminal to the power socket to charge and power the navigator at the same time.

[Note] Please charge the navigator for more than one hour the first time when you use it.

[Note] If the charging indicator flashes in red, it indicates the navigator is charging. The indicator will flash in green when the device is completely charged.

[Note] Please charge the battery in time when the power is insufficient or exhausted in the future. Please keep battery for at least a haft of capacity and store it in cool and dry environment if you won’t use if for long time.

2.2.3 Charging with a vehicle power adaptor

1. Connect one end of the vehicle adapter to the USB interface of the GPS navigator.

2. Connect the other end to vehicle cigarette lighter to power and charge the GPS navigators at the same time.

[Caution] Please plug the vehicle adapter after the car is started, avoiding damages to the navigator caused the instant current at start time.

2.3 Basic Operation

2.3.1 Switching on/off

1. Powr on: Press and hold the power key to turn on the unit.

[Caution] When taking the unit from one place to another place, please wait until the unit conform to the environment, as big fluctuation of humidity would cause short circuit inside the unit.

2. Power off: press and hold the power key, it would prompts Shut down or Sleep. If you just leave the unit for a while you may select Sleep; If you will leave the unit for long time, pelase select Shut.    .

2.3.2 Restarting the system

When the system have no response, press power switch key to shut the system and restart the system.

[Reference] The following cases may cause system failure:

1. Delay and stagnation occur while switching over images;

2. Overlong running time fails to activate the click function;

3. Can’t switch on/off the unit by pressing the power switch.

[Caution] If the system fails, you will miss the system information not yet saved by restarting the system. Please backup the data regularly.

2.3.3 Using the vehicle bracket to fix a navigator

A vehicle bracket is composed of a bracket and a support. Please fix the device using the vehicle bracket onto the front windshield or dashboard while using the GPS navigator in vehicle.

### [Caution] Place the vehicle bracket carefully. Ensure the GPS navigator would not block your driving vision. Ensure the navigator is fixed instead of being placed randomly. Do not fix it where the air bag is placed. Do not place it within the bag's inflation range.

2.3.4 Using a touch pen

The touch pen is used to operate the GPS navigator. Please keep it well.

1. Click: Click the screen once with the nib.

2. Double click: Click the screen twice quickly with the nib.

3. Dragging: Click one place with the nib, then, moves the nib.

[Caution] The touch pen with a broken nib, ballpoint pen, as well as any sharp and rough objects may scratch and damage the LCD screen. Please use a touch pen with a nib in good condition. Do not use the touch pen if the nib is broken.

3. Introduction of Functions

3.1. Description of functions

| Navigation | Open navigation map |
| --- | --- |
| Media | Video player: This is to play wmv/mpeg/mpg/mp4/3gp/asf and avi format video files; this supports progress adjustment, pause, and full-screen play function |
|  | Audio player: This supports WMV, MP3 format audio files and random play, orderly play and cycling play. |
| Image | Image viewer: This is to view JPG, BMP and PNG format files; this allows you to rotate, scale up/down and automatically display images |
| eBook | Ebook: This allows you to read TXT-format files; this allows you to select pages |
| System | This is to set the volume, power supply, back light, date and time, languages as well as system information |

3.2 GPS Navigator

The GPS navigator is applicable for several navigation map softwares. The navigation system pinpoints location of mobile devices by usesing the GPS satellite signal receivers, and displayed in the navigation electronic map. After the user setting the destination, the system will calculate an optimal path automatically to help users reach their destination secure and fast.

The system makes you to fully enjoy the charm of the navigation system by a variety of ways of visual maps, real-time animation, voice prompts, text prompts, etc., and enjoy a pleasant journey

Different navagation maps have difeerent operation steps. Please refer to the instruction of the corresponding navagtion map.

[Note] Before using the navigation function, please purchase the relative map softwares, and specify the route of the map software in the SETTING menu of the navigator.

3.2.1 Read before using the navigation function

3.2.1.1 About map

Due to the development of the transportation, the information in the navigator may differ from the actual transportation even if you are using the latest navigation map. Please drive according to the actual traffic conditions, and comply with the rules and traffic control.

3.2.1.2 About Navigation

The navigator provides navigating routes for your reference. Please decide if you want to drive by compling the route yourself. The route that you are familiar with may be more efficient than the route the navigator suggets.

3.2.1.3 About signals

Factors such as Tall and dense buildings (such as tunnels, between the high-rise buildings, underground car park under the viaduct), weather changes or OFF etc. may affect the signal reception, which results in the navigator can’t position or porsition not veracious, makes the navigation operation failed or functions out gear.

3.4. Multimedia

3.4.1 Music

Click the "Media"\"Music" icon; select the song you want play and click to start playback.

|  | Close | Click to close the audio player |
| --- | --- | --- |
|  | Play | This indicates that a song has been paused or stopped playing; click to continue |
|  | Pause | This indicates a song is being played; click to pause |
|  | Stop | Click to stop playing |
|  | Last | Click to play the last file |
|  | Next | Click to play the next file |
|  | Volume adjustment | Drag the nib of the touch pen on the screen leftward/rightward to adjust the volume. Drag leftward to decrease and rightward to increase |
|  | Progress adjustment | Drag the nib of the touch pen on the screen leftward/rightward to adjust the progress. Drag leftward to back to a certain time and rightward to advance to a certain time to play |
|  | Directory | Click to show all of the audio files in the TF card |
|  | Elapsed time | Click to show the elapsed time |
|  | Normal Play | To play the files in the current folder in order. |
|  | Repeat one | To play the current song repeatedly. |
|  | Random play | To play the songs in the current folder randomly. |
|  | Repeat all | To play all of the songs of the current folder repeatedly. |
|  | Background play | To hide the playing interface and play in background. |

3.4.2 Video

Click the "Media"\"Video" icon; select the video you want play and click to start playback.

|  | Close | Click to close the video player |
| --- | --- | --- |
|  | Play | This indicates that a video has been paused or stopped playing; click to continue |
|  | Pause | This indicates a video is being played; click to pause |
|  | Last | Click to play the last file |
|  | Next | Click to play the next file |
|  | Volume adjustment | Drag the nib of the touch pen on the screen leftward/rightward to adjust the volume. Drag leftward to decrease and rightward to increase |
|  | Progress adjustment | Drag the nib of the touch pen on the screen leftward/rightward to adjust the progress. Drag leftward to back to a certain time and rightward to advance to a certain time to play |
|  | Brightness adjustment | Drag the nib of the touch pen on the screen leftward/rightward to adjust the brightness. |
|  | Time | Elapsed time/ total time of the video. |
|  | File name | Click to show the file name of the playing video. |
|  | Full screen | Doucle click the video area to switch to full screen. |

3.5 Photo

Click “Photo” icon, select the pictures you want to view and click to open.

|  | Close | Click to close the image viewer |
| --- | --- | --- |
|  | Hide | Click to hide the tool bar. |
|  | Rotate clockwise | Click to rotate the current picture clockwise of 90° |
|  | Last | Click to view the last picture in the same folder |
|  | Next | Click to view the next picture in the same folder |
|  | Zoom in | Click to zoom in the current picture. |
|  | Zoom out | Click to zoom out the current picture. |
|  | Directory | Click to show all the picture files in the TF card. |

3.6 EBook

Click “EBook” icon, select the text file you want to read and click to open.

|  | Close | Click it to close the e-Reader. |
| --- | --- | --- |
|  | Last page | Click it to read the last page |
|  | Next page | Click it to read the next page |
|  | Font setting | Click it to enter to set the font. |
|  | Color setting | Click it to enter to set the color of the text, background and selected backgroud. |
|  | Set bookmark | Click and drag the nib to select the current displaying text, and then click the icon to set it as a bookmark. |
|  | Bookmark list | Click to check the bookmarks you saved. |

Font setting interface:

Color Setting interface:

Bookmark list interface:

|  | Close | Click to quit |
| --- | --- | --- |
|  | Decrease | Click to decrease the size of the font. |
|  | Increse | Click to increase the size of the font. |
|  | Adjust | Click to switch to select text color, background and selected background. |
|  | Load bookmark | Select the bookmark you want to load and click this icon. |
|  | Delete bookmark | Select the bookmark you want to delete and click this icon. |

3.7 System Setting

Click the "Setting" button to enter the "setting" menu; then, you can implement relevant settings. The settings cover “Backlight”, "volume", "Language", "GPS Info", "Data Time", "Calibration", “Navi Path”, “Power”, “Restore Set” and "system information".

| Backlight | Click to adjust the brightness of the display. |
| --- | --- |
| Volume | Click to adjust the loudspeaker's volume Switch on/off screen click sound |
| Language | Click to set the prompt language |
| GpsInfo | Click to display the satellite signals it received. |
| Date Time | This is to set the system time and date and show the system time zone |
| Calibration | Click to cabibrate the touch panel. |
| Navi Path | Click to set the path of the navigation e-map. |
| Power | Click to check current battery status |
| Restore Set | Click to restore default settings. |
| System information | This allows you to reset the device to factory defaults, and implement GPS reset and touch screen calibration. |

3.7.1 Backlight

|  | Close | Click to quit the brightness setting application |
| --- | --- | --- |
|  | Brightness down | Click to decrease the brightness level by level until it is minimized |
|  | Brightness up | Click to increase the brightness level by level until it is maximized |
|  | Adjust | Click to switch to select the time of auto OFF. |
|  | Brightness display | The yellow bars refer to the current brightness |

3.7.2 Volume Setting

The volume setting is shown as Figure 8-2:

1. Loudspeaker's volume adjustment; 2. Setting of "Screen Click Sound”. 3. FM transmission (details as "8.2 FM transmission setting" content).

|  | Close | Click to quit the volume setting application |
| --- | --- | --- |
|  | Decrease Volume | Click to decrease the volume level by level until it is minimized |
|  | Increase Volume | Click to increase the volume level by level until it is maximized |
|  | Adjust | Click to switch to select Loud, Soft or OFF. |
|  | Current Volume | The yellow bars refer to the current volume. |

3.7.3 Language Setting

Click the button [ ] or [ ] in the language bar to select a system language.

3.7.4 GPS Information

To display the information of the satellite signals. After position, it displays the information of latitude, longitude, altitude and speed etc. The status bar  displays the number of the satellite. You may click “Reset” icon to make the GPS re-search for satellite.

3.7.5 Date and Time

The time and date settings are shown as :

1. System date setting; 2. System time setting. 3. Time zone setting

- Click  or  icon to set the year, month, day and time.

- Click  or  icon to set the time zone.

3.7.6 Caliration

Click the button “Calibration” icon to prompt the “Touch Screen Calibration” interface. Click the cross center with the touch pen and the cursor moves towards the center, top left corner, bottom left corner, top right corner and bottom right corner until successful positioning. The system will close the interface automatically and back to system interface.

3.7.7 Navigation Path

As the followng picture shows:

Click  icon to select the file of map that saved in the TF card or the flash memory of the unit.

3.7.8 Battery Power

The main functions for “Power” is to check the current remaining energy of the battery.

3.7.9 Restore Set

Click the “Restore set” icon, it prompts “Are you sure to restore default settings?” Click the button  to reset the device to factory defaults; click  to close the “Factory Defaults” interface.

3.7.10 System Information

Click to display the information of the current software version.

Troubleshooting

If your GPS navigator fails to work, please check it following the solutions below. If the problem still exists, please contact our customer service center.

| Failures | Causes | Solutions |
| --- | --- | --- |
| The device does not turn on | The battery energy is insufficient | Power the system with external power source and charge the battery at the same time |
|  | The batter switch is off | Switch upward the battery switch |
| The device turns off during use | The battery energy is insufficient | Power the system with external power source and charge the battery at the same time |
| The device fails to display; The display contents are not clear | The back light brightness is too low, The back light is turned off automatically | Adjust the brightness using the touch pen to click the LCD screen. The back light will be on again. |
| No right actions occur on clicking the button | The touch screen is not calibrated. | Calibrate the touch screen again |
| There is no sound while playing | The volume is set too low | Increase the volume |
|  | The earphone is in poor contact | Plug the earphone properly |
| The device can not access a computer | The USB cable fails to connect | Connect the USB cable properly |
| The device can not receive the GPS signals |  | It depends on whether local GPS satellite signals are strong or weak. Wait for three minutes above to receive signals |
| The map data is missing inadvertently |  | 1. There are map files stored in the disk. 2. Contact your agent or dealer to ask for a password that is required when the navigation function is activated again. |

# Text boxes

User Manual

Guarantee Card