NIHON KOSO CO., LTD.

# STRUCTURAL ANALYSIS

# OF UNITS AND PARTS

# DN50 CONTROL VALVE

510D-3-6,67/230-50 РР3

For NPP

2014

CONTENTS

|  |  | Page |
| --- | --- | --- |
|  | Introduction……………………………………………………………… | 3 |
| 1. | Initial Data…………………………..……………………… | 3 |
| 2. | Hydraulic test Scoping……………………………………… | 5 |
| 3. | Body Static Strength calculation…………………………… | 5 |
| 4. | Calculation of bonnet flange joint……………………………………… | 8 |
|  | 4.1 Flanged joint studs strength……………………………… | 8 |
|  | 4.2 Strength of body inner thread………………………… | 9 |
|  | 4.3 Strength of nut thread…………………………………… | 9 |
|  | 4.4 Bonnet flange strength……………………………..…… | 10 |
| 5. | Calculation of gland seal unit………………………………………… | 11 |
| 6. | Strength calculation for studs, nuts and trip bar … 6.1 Stud thread strength………………………… 6.2 Strength of nut thread…………………… 6.3 Strength of thread in bonnet………………………… 6.4 Trip bar calculation …… | 11 11 12 12 13 |
|  | Conclusion……………………………………………… | 14 |
|  | List of References………………………………………………… | 14 |
|  | Record of changes……………….……………………… | 15 |

Introduction.

The purpose of valve units and parts strength analysis is:

- The verification of satisfying the conditions of static, cyclic strength for valve units and parts.

DN50 control valve units and parts strength analysis is performed in compliance with:

- Drawing 510D-3-6,67/230-50 и 510D-3-6,67/230-50.1;

- «Rules on strength calculation of equipment and pipelines of nuclear power plants», ПНАЭ Г-7-002-86 /1/;

-«Piping valves for nuclear power plants. General specifications», НП-068-05 /2/;

Valve units and parts strength analysis according to Table 1.

Table 1.

| Name | Method of control | Body material | Bore diameter, d, mm. |
| --- | --- | --- | --- |
| 510D-3-6,67/230-50 510D-3-6,67/230-50.1 | Electric drive Electric drive | A216-WCB A216-WCB | 49 49 |

1. Initial data.

DN 50 control valve is designed for installation at injection/spray pipeline of cooling water to QRDS-SN at nuclear power plant as a regulating/control device/instrument.

- design pressure and temperature: see table 2;

- working medium: water;

- body material: A216-WCB;

- piping nipple loads /2/:

Table 2.

| Designation | Material | Load class and value |
| --- | --- | --- |
|  |  | Normal operating conditions kN(m | Normal operating conditions kN |
|  |  | = 6,67MPa; Т = 230(C |
| 510D-3-6,67/230-50 510D-3-6,67/230-50.1 | A216-WCB | 0,756 0,756 | 3,25 3,25 |

- See Table 3 for body material mechanical properties:

Table 3.

| Parameter | Designation | Calculating formula (source) | Design temperature, °С | Unit |
| --- | --- | --- | --- | --- |
|  |  |  | A216-WCB |  |
|  |  |  | 20°C | 300 |  |
| Minimum yield strength at design temperature |  | Certificate | 250 | 220 | MPa |
| Minimum ultimate strength at design temperature |  | certificate | 485 | 400 | MPa |
| Elasticity modulus at design temperature |  | certificate | 200 | 180 | GPa |
| Temperature coefficient of linear expansion |  | certificate | - | 15 | uK-1 |
| Nominal allowable stress |  |  | 166,7 | 146,7 | MPa |
| Allowable stress |  |  | 166,7 | 146,7 | MPa |
| Allowable stress |  |  | 216,7 | 190,7 | MPa |
| Allowable stress |  |  | 496,1 | 429 | MPa |
| Allowable coefficient of total damage |  | ПНАЭГ-7-002-86 | 1 | 1 | - |
| Specimen contraction at design temperature |  | ПНАЭГ-7-002-86 | 40 | 40 | % |

2. Hydraulic test scoping.

Hydraulic test scoping was performed in compliance with:

- «Rules of arrangement and safe operation of equipment and pipelines of nuclear power plants», ПНАЭ Г-7-008-89 /3/.

Hydraulic test scoping according to Table 4.

Table 4.

| Parameters | Designation | Calculating formula (source) | Value | Units |
| --- | --- | --- | --- | --- |
| Design pressure |  | Table 1 | 6,67 | MPa |
| Coefficient |  | /3/ | 1,25 | - |
| Nominal allowable stress at hydraulic test temperature |  | Table 3 | 166,7 | MPa |
| Nominal allowable stress at design temperature |  | Table 3 | 146,7 | MPa |
| Hydraulic test lower limit |  | / | 9,47 | MPa |
| Body outlet inner diameter |  | Drawing | 0,049 | м |
| Body outlet outer diameter |  | Drawing | 0,057 | м |
| Body outlet wall thickness |  |  | 0,004 | м |
| Hydraulic test upper limit |  |  | 33,96 | MPa |

Body hydraulic testing is allowed at pressure of 9,5 MPa - 33,9 MPa for A216-WCB.

Upper pressure is limited with 12 MPa, as far as further hydraulic test pressure increase may cause fastener deformation.

3. Body static strength analysis

The analysis of actual loads caused with pipelines and internal pressure shows that the highest stress valve part determining item/product static strength is the part with minimum relative thickness of walls – the area of nipple edges preparation for piping.

Body static strength analysis according to Table 5.

Table 5.

| Parameters | Designation | Calculating formula (source) | Value | Units |
| --- | --- | --- | --- | --- |
|  |  |  | A216-WCB |  |
| 1 | 2 | 3 | 4 | 5 |
| Design pressure | Р | Table 1 | 6,67 | MPa |
| Design temperature | Т | Table 1 | 300 | (С |
| Body outlet inner diameter |  | Drawing | 0,049 | m |
| Body outlet outer diameter |  | Drawing | 0,057 | m |
| Body outlet wall thickness |  |  | 0,004 | m |
| Inner diameter tolerance |  | Drawing | 0,00062 | м |
| Outer diameter tolerance |  | Drawing | 0,0005 | m |
| Body outlet wall corrosion |  | [1] | 0,0003 | m |
| Design allowance for body outlet wall thickness |  |  | 0,00086 | m |
| Design allowance for body outlet wall thickness without regard to corrosion |  |  | 0,00056 | m |
| Reduced stress in body outlet walls |  |  | 55,38 | MPa |
| Allowable stress at ТР |  | Table 3 | 146,7 | MPa |
| Safety factor for allowable stress |  |  | 2,65 | - |
| Body outlet section modulus | W |  | 6,91E-06 | m3 |
| Piping weight load moment at normal operating conditions |  | Table 2 | 756 | Nm |
| Stress caused with piping weight load moment |  |  | 109,36 | MPa |
| Body outlet cross-section area | F |  | 5,50E-04 | m2 |
| Piping weight load force |  | Table 2 | 3250 | N |
| Stress caused with piping weight load force |  | / F | 5,91 | MPa |

Table 5 continued.

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Stress under weight load at normal operating conditions and internal pressure |  | ++ | 170,65 | MPa |
| Allowable stress |  | Table 3 | 429,0 | MPa |
| Safety factor for allowable stress |  | / | 2,51 | - |

CONCLUSION:

1) Strength condition for general membrane stress:

< is SATISFIED;

2) Strength condition for membrane and general bending stress:

< is SATISFIED;

4. Calculation of bonnet flange joint.

Calculation of bonnet flange joint is performed according to Table 6.

Table 6.

| Parameters | Designation | Calculating formula (source) | Value | Units |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| Mean diameter of gasket seal face |  | Drawing | 0,0915 | m |
| Gasket seal face outer diameter |  | Drawing | 0,096 | m |
| Gasket effective width | B | Drawing | 0,009 | m |
| Gasket tightness supporting coefficient | M | /4/ | 2 | - |
| Force for gasket tightness supporting at hydraulic test pressure |  | .Рг | 51716 | N |
| Hydrostatic load at gasket mean diameter caused with pressure |  | Рг/4 | 65722 | N |
| Accepted load at gasket |  | + | 117438 | N |
| Stud thread diameter |  | Drawing | 0,014 | m |
| No. of studs |  | Drawing | 10 | - |
| Coefficient accounting for surface condition and thread lubrication |  | /5/ | 0,26 | - |
| Torque at thread while tightening |  |  | 42,75 | Nm |
| 4.1 Flanged joint studs strength |
| Parameters | Designation | Calculating formula (source) | Value | Units |
| 1 | 2 | 3 | 4 | 5 |
| Maximum force of valve displacement |  | Technical requirements for drives | 23000 | N |
| Rated force at studs |  | + | 140438 | N |
| Stud non-threaded/round part diameter |  | Drawing | 0,01262 | m |
| Tensile stress in studs |  |  | 112,27 | MPa |
| Material of studs | - | Drawing | A193-B7 |  |
| Yield strength at operating temperature |  | certificate | 520 | MPa |

Table 6 continued.

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Nominal allowable stress |  | /2 | 260 | MPa |
| Safety factor |  | / | 2,32 | - |
| Thread performance factor |  | /5/ | 0,75 | - |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height |  | Drawing | 0,014 | m |
| Thread inner diameter |  | Drawing | 0,0115 | m |
| Thread shear stress |  |  | 49,39 | MPa |
| Allowable shear stress |  | /2 | 130 | MPa |
| Shear stress safety factor |  | / | 2,63 | - |
| 4.2 Strength of body inner thread |
| Rated force at studs |  | + | 140438 | N |
| Yield strength at operating temperature |  | certificate | 220 | MPa |
| Nominal allowable stress |  | /2 | 110 | MPa |
| Thread performance factor |  | /5/ | 0,87 | - |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height |  | Drawing | 0,016 | m |
| Thread inner diameter |  | Drawing | 0,0115 | m |
| Thread shear stress |  |  | 37,25 | MPa |
| Allowable shear stress |  | /2 | 55 | MPa |
| Shear stress safety factor |  | / | 1,48 | - |
| 4.3 Strength of nut thread |
| Rated force at studs |  | + | 140438 | N |
| Material of nut | - | Drawing | A194-2H |  |
| Yield strength at operating temperature |  | certificate | 225 | MPa |
| Nominal allowable stress |  | /2 | 112,5 | MPa |
| Thread performance factor |  |  | 0,87 | - |

Table 6 continued.

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height | H | /5/ | 0,014 | m |
| Thread inner diameter |  | Drawing | 0,0115 | m |
| Thread shear stress |  |  | 42,57 | MPa |
| Allowable shear stress |  | /2 | 56,25 | MPa |
| Shear stress safety factor |  | / | 1,32 | - |
| 4.4 Bonnet flange strength |
| Cover thickness in design section |  | Drawing | 0,029 | m |
| Design section diameter |  | Drawing | 0,097 | m |
| Stud outer diameter |  | Drawing | 0,118 | m |
| Design section bending arm |  |  | 0,0105 | m |
| Bending stress |  |  | 34,54 | MPa |
| Material of bonnet | - | Drawing | A105 |  |
| Yield strength at operating temperature |  | certificate | 230 | MPa |
| Allowable bending stress |  | 1,3 | 299 | MPa |
| Safety factor |  | / | 8,66 | - |

5. Calculation of gland seal unit.

Calculation of gland seal unit is performed according to Table 7.

Table 7.

| Parameters | Designation | Calculating formula (source) | Value | Units |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| Stem diameter | d | Drawing | 0,017 | m |
| Chamber diameter | D | Drawing | 0,027 | m |
| Coefficient | φ | /5/ | 1,5 | - |
| Gland tightening force | Q | π(D2-d2)P*φ | 13822,908 | N |
| Stud thread diameter |  | Drawing | 0,008 | m |
| No. of studs |  | Drawing | 2 | - |
| Coefficient accounting for surface condition and thread lubrication |  | /5/ | 0,26 | - |
| Torque at thread while tightening |  | Q/ | 14,37582432 | Nm |

6. Strength calculation for studs, nuts and trip bar.

Strength calculation for studs, nuts and trip bar according to Table 8.

Table 8

| Parameters | Designation | Calculating formula (source) | Value | Units |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| 6.1 Stud thread strength |
| Force caused at studs with stem under condition of stem end stop at gland ring at opening |  | Drawing | 0 | N |
| Rated force at studs |  | + | 13822,908 | N |
| Stud non-threaded/round part diameter |  | Drawing | 0,012 | m |
| Tensile stress in studs |  |  | 61,11 | MPa |
| Material of studs | - | Drawing | A193-B8 |  |
| Yield strength at operating temperature |  | certificate | 270 | MPa |

Table 8 continued.

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Nominal allowable stress |  | /2 | 135 | MPa |
| Safety factor |  | / | 2,21 | - |
| Thread performance factor |  | /5/ | 0,75 | - |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height |  | Drawing | 0,012 | m |
| Thread inner diameter |  | Drawing | 0,0066 | m |
| Thread shear stress |  |  | 49,41 | MPa |
| Allowable shear stress |  | /2 | 67,5 | MPa |
| Shear stress safety factor |  | / | 1,37 | - |
| 6.2 Strength of nut thread |
| Rated force at studs |  | + | 13822,91 | N |
| Material of nut | - | Drawing | A194-8 |  |
| Yield strength at operating temperature |  | certificate | 267 | MPa |
| Nominal allowable stress |  | /2 | 133,5 | MPa |
| Thread performance factor |  | /5/ | 0,87 | - |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height | H | /5/ | 0,008 | m |
| Thread inner diameter |  | Drawing | 0,0066 | m |
| Thread shear stress |  |  | 63,89 | MPa |
| Allowable shear stress |  | /2 | 66,75 | MPa |
| Shear stress safety factor |  | / | 1,04 | - |
| 6.3 Strength of thread in bonnet |
| Rated force at studs |  | + | 13822,91 | N |
| Material of bonnet | - | Drawing | A105 |  |
| Yield strength at operating temperature |  | certificate | 230 | MPa |
| Nominal allowable stress |  | /2 | 115 | MPa |
| Thread performance factor |  | /5/ | 0,87 | - |

Table 8 continued.

| 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- |
| Thread turns deformation factor |  | /5/ | 0,75 | - |
| Thread height |  | Drawing | 0,012 | m |
| Thread inner diameter |  | Drawing | 0,0066 | m |
| Thread shear stress |  |  | 42,59 | MPa |
| Allowable shear stress |  | /2 | 57,5 | MPa |
| Shear stress safety factor |  | / | 1,35 | - |
| 6.4 Trip bar calculation |
| Trip bar thickness |  | Drawing | 0,015 | m |
| Trip bar width |  | Drawing | 0,057 | m |
| Hole diameter |  | Drawing | 0,02 | m |
| Outer diameter of circular bearing surface |  | Drawing | 0,03 | m |
| Circular bearing surface slope angle |  | Drawing | 20 | deg. |
| Studs centre-to-centre distance |  | Drawing | 0,04 | m |
| Trip bar design thickness |  |  | 0,009 | m |
| Moment of resistance of inertia of trip bar |  |  | 1,09142E-06 | m3 |
| Circular bearing surface mean diameter |  |  | 0,025 | m |
| Arm of bending moment caused with support reaction force |  |  | 0,008 | m |
| Force at bar caused with stud |  |  | 6911,454 | N |
| Bending moment |  |  | 83,20 | Nm |
| Trip bar bending stress |  | / | 76,23 | MPa |
| Material of trip bar | - | Drawing | А479-304 | - |
| Material yield strength at design temperature |  | certificate | 205 | MPa |
| Material stress limit at design temperature |  | certificate | 515 | MPa |
| Safety factor for yield strength |  | / | 2,69 | - |
| Safety factor for stress limit |  | / | 6,76 | - |

CONCLUSION

The analysis showed that valve configuration, chosen dimensions and the properties constructional material satisfy the strength limits and provide valve operation at specified parameters.

List of References

- «Rules on strength calculation of equipment and pipelines of nuclear power plants». ПН АЭ Г-7-002-86.

- НП-068-05, Piping valves for nuclear power plants. General specifications.- М.: 2005.

- «Rules of arrangement and safe operation of equipment and pipelines of nuclear power plants», ПНАЭ Г-7-008-89

- Certificates for materials.

- Gurevich D.F. Design and calculation of piping vales. – M.: Mashinostroenie, 1969.

- Birger I.A. et al. Machine parts strength calculation. – M.: Mashinostroenie, 1993

- Anuriev V. I. et al. Handbook of engineering designer. – M.: Mashinostroenie, 1999.

- Expert report on possibility of imported materials use for production of QRDS for BNPP-2 by KOSO Company.

RECORD OF CHANGES

| Changes | Sheet nos. | Document sheets total | Document no. | Accompanying document registration no. | Signature | Date |
| --- | --- | --- | --- | --- | --- | --- |
|  | Changed | Replaced | New | Cancelled |  |  |  |  |  |

# Text boxes

APPROVED BY:

Valve Construction

Department Manager

Nihon Koso Co., Ltd.

_________M. Katayama

«___»  ______________ 2014