Environment protection

The provisions to ensure reliability of water basin protection

Industrial sewage of demineralized water generator system is originated as a result of:

( Washing of the first group mechanical filters (clearing of water for the cooling tower) in amount of 305 m3/h; 300 m3/day; 109500 m3/year;

( Washing of the second group mechanical filters (clearing of water upstream of the ultrafiltration installation) in amount of 305 m3/h; 500 m3/day; 182500 m3/year;

( Backwashing of the ultrafiltration installation in amount of 368 m3/h; 1074 m3/day; 392010 m3/year;

( Blow-down of the reverse osmosis plant in amount of 132 m3/h; 3168 m3/day; 1156320 m3/year;

( Loosening of the second stage H-cation filters in amount of 102.24 m3/h; 51.12 m3/day; 8177 m3/year;

( Regeneration of the second stage H-cation filters in amount of 71 m3/h; 52.83 m3/day; 8450 m3/year;

( Washing out of the second stage H-cation in amount of 71 m3/h; 85.20 m3/day; 13628;

( Loosening of the second stage anion-exchange filters in amount of 77 m3/h; 38.34 m3/day; 4565 m3/year;

( Regeneration of the second stage anion-exchange filters in amount of 28.4 m3/h; 19.4 m3/day; 3744 m3/year;

( Scrubbing of the second stage anion-exchange filters in amount of 49.7 m3/h; 67.45 m3/day; 13016 m3/year;

( Loosening of mixed bed filters in amount of 15.1 m3/h; 30.1 m3/day; 2201 m3/year;

( Regeneration of mixed bed filters by acid in amount of 16.0 m3/h; 4.32 m3/day; 315 м3/year;

( Regeneration of mixed bed filters by alkali in amount of 13.5 m3/h; 4.52 m3/day; 330 m3/year;

( Acid scrubbing of mixed bed filters in amount of 25.2 m3/h; 28.26 m3/day; 2063;

( Alkali scrubbing of mixed bed filters in amount of 25.2 m3/h; 47.10 m3/day; 3438 m3/year;

Backwashing, regeneration water and washing waters from H-cation and anion-exchange filters and mixed bed filters (MBF) enter the neutralization tank where their mixing and self-neutralization occurs, also acid and alkali for full neutralization are fed into the neutralization tank. The pH-meter is installed in the waste line from the neutralization tank for continuous analysis of hydrogen ionization value in a stream.

Waste washing effluent from mechanical filters, blow-down water from the reverse osmosis plant, backwashing water from the ultrafiltration installation are also discharged through the neutralization tank.

After neutralization and bringing of рН-value of a solution to the standard value, the mineralized discharge from the neutralization tank goes to the pumped collecting drain and further to the factory treatment facilities.

Demineralized water generator system is based on the advanced hyperfiltration (reverse osmosis) technology which does not introduce additional salts in a cycle. Blow-down of reverse osmosis apparatuses contains only the salts which have entered with initial water.

The qualitative and quantitative composition of industrial sewage is presented in table 10.1

Table 10.1 The sewage

| Name of waste water discharged, section, apparatus | Discharge place | Number of flows, m3/day | Periodicity of waste discharge | Discharge characteristic |
| --- | --- | --- | --- | --- |
|  |  |  |  | Controllable harmful substances content in waste discharge (by components), mg/l | MAC in reservoir water and MAC for fish industry of harmful substances discharged, mg/l | Allowable concentration of harmful substances discharged, kg/day | Notes |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 10.1.1 Washing effluent from the first group mechanical filters (water cleaning for the cooling tower) | Into the neutralization tank 13.1-13.2 | 300 | Periodically with the constant discharge (3 times a day for 20 minutes) | Са 2 + | 477.5 | - | 143.25 |  |
|  |  |  |  | Mg 2 + | 79.6 | 50 | 23.88 |  |
|  |  |  |  | Na + | 40.1 | 200 | 12.03 |  |
|  |  |  |  | SO4 2 | 519.2 | 500 | 155.76 |  |
|  |  |  |  | Cl - | 183.5 | 350 | 55.05 |  |
|  |  |  |  | NO3 - | 11.3 | 45 | 3.39 |  |
|  |  |  |  | NO2 - | 0.1 | 3.3 | 0.03 |  |
|  |  |  |  | SiO3 2 | 12.6 | - | 3.78 |  |
|  |  |  |  | Total iron | 5.04 | 0.3 (1) | 1.51 |  |
|  |  |  |  | Suspended substances | 40.0 | - | 12.0 |  |
|  |  |  |  | Salinity | 2327.5 | - | 698.25 |  |
|  |  |  |  | рН | 8 | - | 8 |  |
| 10.1.2 Washing effluent of the second group mechanical filters (water cleaning for the ultrafiltration installation) | Into the neutralization tank 13.1-13.2 | 500 | Periodically with the constant discharge (5 times a day for 20 minutes) | Са 2 + | 477.5 | - | 238.75 |  |
|  |  |  |  | Mg 2 + | 79.6 | 50 | 39.8 |  |
|  |  |  |  | Na + | 40.1 | 200 | 20.05 |  |
|  |  |  |  | SO4 2 | 519.2 | 500 | 259.6 |  |
|  |  |  |  | Cl - | 183.5 | 350 | 91.75 |  |
|  |  |  |  | NO3 - | 11.3 | 45 | 5.65 |  |
|  |  |  |  | NO2 - | 0.1 | 3.3 | 0.05 |  |
|  |  |  |  | SiO3 2 | 12.6 | - | 6.3 |  |
|  |  |  |  | Total iron | 9.14 | 0.3 (1) | 4.57 |  |

| Table 10.1 continuation |
| --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
|  |  |  |  | Suspended substances | 73 | - | 36.5 |  |
|  |  |  |  | Salinity | 2327.5 | - | 1163.75 |  |
|  |  |  |  | рН | 8 | - | 8 |  |
| 10.1.3 Backwashing discharge water from the ultrafiltration installation | Into the neutralization tank 13.1-13.2 | 368 | Periodic with the constant discharge (at intervals of an hour for 1 minute) | Са 2 + | 119.45 | - | 128.3 |  |
|  |  |  |  | Mg 2 + | 19.9 | 50 | 21.4 |  |
|  |  |  |  | Na + | 10.07 | 200 | 10.8 |  |
|  |  |  |  | SO4 2 | 129.89 | 500 | 139.5 |  |
|  |  |  |  | Cl - | 40.59 | 350 | 43.6 |  |
|  |  |  |  | NO3 - | 2.82 | 45 | 3.0 |  |
|  |  |  |  | NO2 - | 0.03 | 3.3 | 0.03 |  |
|  |  |  |  | SiO3 2 | 2.49 | - | 2.7 |  |
|  |  |  |  | Total iron | 6.21 | 0.3 (1) | 6.7 |  |
|  |  |  |  | Suspended substances | 49.3 | - | 52.9 |  |
|  |  |  |  | Salinity | 568 | - | 610 |  |
|  |  |  |  | рН | 8 | - | 8 |  |
| 10.1.4 Blow-down water from the reverse osmosis plant (ROP) | Into the neutralization tank 13.1-13.2 | 132 | Continuous with the constant discharge | Са 2 + | 477.5 | - | 1130.7 |  |
|  |  |  |  | Mg 2 + | 79.6 | 50 | 188.5 |  |
|  |  |  |  | Na + | 40.1 | 200 | 94.96 |  |
|  |  |  |  | SO4 2 | 519.2 | 500 | 1229.46 |  |
|  |  |  |  | Cl - | 183.5 | 350 | 434.53 |  |
|  |  |  |  | NO3 - | 11.3 | 45 | 26.76 |  |
|  |  |  |  | NO2 - | 0.1 | 3.3 | 0.23 |  |
|  |  |  |  | SiO3 2 | 12.61 | - | 29.84 |  |
|  |  |  |  | Salinity | 2327.5 | - | 5511.5 |  |
|  |  |  |  | рН | 8 | - | 8 |  |
| 10.1.5 Backwashing waters of II stage N-filters | Into the neutralization tank 13.1-13.2 | 102.24 | Periodic with the constant discharge (1 time a day for 30 minutes) | Conditionally waters alone |  |
| 10.1.6 Regeneration waters of II stage N-filters | Into the neutralization tank 13.1-13.2 | 71 | Periodic with the constant discharge (1 time a day for 45 minutes) | Са 2 + | 1194 | - | 63.1 |  |
|  |  |  |  | Mg 2 + | 199 | 50 | 10.5 |  |
|  |  |  |  | Na + | 100.3 | 200 | 5.3 |  |
|  |  |  |  | SO4 2 | 11849 | 500 | 626 |  |
|  |  |  |  | Н + | 167 | - | 8.8 |  |
|  |  |  |  | Salinity | 13507.5 | - | 713.6 |  |
|  |  |  |  | рН | 2.5 | - | 2.5 |  |
| 10.1.7 Scrubbing waters of II stage N-filters | Into the neutralization tank 13 | 71 | Periodic with the constant discharge (1 time a day for 72 minutes) | Са 2 + | 185.4 | - | 15.8 |  |
|  |  |  |  | Mg 2 + | 30.5 | 50 | 2.6 |  |
|  |  |  |  | Na + | 15.3 | 200 | 1.3 |  |
|  |  |  |  | SO4 2 | 1837 | 500 | 156.5 |  |
|  |  |  |  | Н + | 25.8 | - | 2.2 |  |
|  |  |  |  | Salinity | 2094 | - | 178.4 |  |
|  |  |  |  | рН | 3.5 | - | 3.5 |  |
| 10.1.8 Backwashing waters of II stage OH-filters | Into the neutralization tank 13 | 77 | Periodic with the constant discharge (1 time a day for 30 minutes) | Conditionally waters alone |  |
| 10.1.9 Regeneration waters of II stage OH-filters | Into the neutralization tank 13.1-13.2 | 28.4 | Periodic with the constant discharge (1 time a day for 41 minutes) | Na + | 19191 | 200 | 372.3 |  |
|  |  |  |  | SO4 2 | 2918 | 500 | 56.6 |  |
|  |  |  |  | Cl - | 1031 | 350 | 20 |  |
|  |  |  |  | NO3 - | 62 | 45 | 1.2 |  |
|  |  |  |  | SiO3 2 | 72 | - | 1.4 |  |
|  |  |  |  | OH - | 11582 | - | 224.7 |  |
|  |  |  |  | Salinity | 38464 | - | 746.2 |  |
|  |  |  |  | рН | 13 | - | 13 |  |
| 10.1.10 Scrubbing waters of II stage OH-filters | Into the neutralization tank 13 | 49.7 | Periodic with the constant discharge (1 time a day for 81 minutes) | Na + | 1380 | 200 | 93.1 |  |
|  |  |  |  | SO4 2 | 210 | 500 | 14.2 |  |
|  |  |  |  | Cl - | 74 | 350 | 5.0 |  |
|  |  |  |  | NO3 - | 4.45 | 45 | 0.3 |  |
|  |  |  |  | SiO3 2 | 4.45 | - | 0.3 |  |
|  |  |  |  | OH - | 833 | - | 56.2 |  |
|  |  |  |  | Salinity | 2766.5 | - | 186.6 |  |
|  |  |  |  | рН | 12 | - | 12 |  |
| 10.1.11 Backwashing waters of mixed bed filters | Into the neutralization tank 13.1-13.2 | 15.1 | Periodic with the constant discharge (1 time a day for 30 mines, 2 times a month) | Conditionally waters alone |  |
| 10.1.12. Regeneration acid waters from mixed bed filters | Into the neutralization tank 13.1-13.2 | 16 | Periodic with the constant discharge (1 time a day for 30 minutes) | Na + | 1000 | 200 | 4.32 |  |
|  |  |  |  | SO4 2 | 23924 | 500 | 103.35 |  |
|  |  |  |  | Н + | 456 | - | 1.97 |  |
|  |  |  |  | Salinity | 25380 | - | 109.64 |  |
|  |  |  |  | рН | 2.0 | - | 2.0 |  |
| 10.1.13 Regeneration alkaline water from mixed bed filters | Into the neutralization tank 13.1-13.2 | 13.5 | Periodic with the constant discharge (1 time a day for 30 minutes) | Na + | 19173 | 200 | 86.66 |  |
|  |  |  |  | SO4 2 | 115 | 500 | 0.52 |  |
|  |  |  |  | Cl - | 84.1 | 350 | 0.38 |  |
|  |  |  |  | SiO3 2 | 288 | - | 1.3 |  |
|  |  |  |  | OH - | 13962 | - | 63.11 |  |
|  |  |  |  | Salinity | 33622 | - | 151.97 |  |
|  |  |  |  | рН | 13 | - | 13 |  |
| 10.1.14 Scrubbing acid waters from mixed bed filters | Into the neutralization tank 13.1-13.2 | 25.2 | Periodic with the constant discharge (1 time a day for 30 minutes) | Na + | 38.2 | 200 | 1.08 |  |
|  |  |  |  | SO4 2 | 914.4 | 500 | 25.84 |  |
|  |  |  |  | Н + | 17.3 | - | 0.49 |  |
|  |  |  |  | Salinity | 970 | - | 27.41 |  |
|  |  |  |  | рН | 3.0 | - | 3.0 |  |

| Table 10.1 termination |
| --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| 10.1.15 Scrubbing alkaline water from mixed bed filters | Into the neutralization tank 13.1-13.2 | 25.2 | Periodic with the constant discharge (1 time a day for 30 minutes) | Na + | 460 | 200 | 21.67 |  |
|  |  |  |  | SO4 2 | 2.76 | 500 | 0.13 |  |
|  |  |  |  | Cl - | 2.12 | 350 | 0.1 |  |
|  |  |  |  | SiO2 | 6.79 | - | 0.32 |  |
|  |  |  |  | OH - | 335 | - | 15.78 |  |
|  |  |  |  | Salinity | 806.6 | - | 37.99 |  |
|  |  |  |  | рН | 12 | - | 12 |  |
| 10.1.16 Discharge water from the neutralization tank | In the pumped collecting drain of the factory | 250 | Continuous with the variable discharge | Са 2 + | 377.5 | - | 1719.9 |  |
|  |  |  |  | Mg 2 + | 62.9 | 50 | 286.7 |  |
|  |  |  |  | Na + | 133.8 | 200 | 609.8 |  |
|  |  |  |  | SO4 2 | 638.0 | 500 | 2907.1 |  |
|  |  |  |  | Cl - | 142.6 | 350 | 649.9 |  |
|  |  |  |  | NO3 - | 8.9 | 45 | 40.3 |  |
|  |  |  |  | NO2 - | 0.1 | 3.3 | 0.31 |  |
|  |  |  |  | SiO3 2 | 9.7 | - | 44.3 |  |
|  |  |  |  | Salinity | 2147.8 | - | 9785.9 |  |
|  |  |  |  | Total iron | 2.8 | 0.3 (1) | 12.7 |  |
|  |  |  |  | Suspended substances | 22.3 | - | 101.4 |  |
|  |  |  |  | рН | 8.0 | - | 8.0 |  |

Sewage formation flow diagram

Industrial sewage

# Text boxes

Washing effluent of the second group mechanical filters

Waste treatment facilities

230 m3/day

47,10 m3/day

28,26 m3/day

4,52 m3/day

4,32 m3/day

30,1 m3/day

67,45 m3/day

19,4 m3/day

Continuous with the constant discharge

Periodically with the constant discharge, 3 times a day for 20 minutes

38,34 m3/day

85,2 m3/day

52,83 m3/day

51,2 m3/day

3168 m3/day

1074 m3/day

500 m3/day

300 m3/day

Neutralization tank

13.1-13.2

Periodic with the constant discharge (1 time a day for 30 minutes

Periodic with the constant discharge (1 time a day for 30 minutes

Periodic with the constant discharge 1 time a day for 30 minutes

Periodic with the constant discharge 1 time a day for 30 minutes

Periodic with the constant discharge 1 time a day for 41 minutes

Periodic with the constant discharge 1 time a day for 81 minutes

Periodic with the constant discharge 1 time a day for 30 mines, 2 times a month

Periodic with the constant discharge 1 time a day for 30 minutes

Periodic with the constant discharge 1 time a day for 72 minutes

Periodic with the constant discharge 1 time a day for 45 minutes

Periodic with the constant discharge at intervals of an hour for 1 minute

Periodically with the constant discharge 5 times a day for 20 minutes

Periodic with the constant discharge 1 time a day for 30 minutes

Regeneration acid waters from mixed bed filters

Backwashing waters of mixed bed filters

Scrubbing alkaline water from mixed bed filters

Scrubbing acid waters from mixed bed filters

Regeneration alkaline water from mixed bed filters

Scrubbing waters of II stage OH-filters

Regeneration waters of II stage OH-filters

Backwashing waters of II stage OH-filters

Scrubbing waters of II stage N-filters

Regeneration waters of II stage N-filters

Backwashing waters of II stage N-filters

Blow-down water from the reverse osmosis plant

Backwashing discharge water from the ultrafiltration installation

Washing effluent of the first group mechanical filters